## Slide 1: Procedural Game Sound Effects in x86-64 Assembly
Every audio sample is computed by hand-written NASM; Python only draws the buttons
Allein Edward Miranda · Jan Emil Stenland · Jose Gian M. Tubera · Ray A. Nicolas
CA010 Computer Architecture and Organization · College of Computer Studies, Angeles University Foundation
Notes: "Hi everyone. Our project is a sound-effect generator for retro-style video games. Think of the coin sound in Mario, or a laser in an old arcade game. You pick a sound, adjust it with sliders, and the program builds that sound from scratch. The interesting part is that the piece that actually calculates the sound is written in Assembly. Assembly is the lowest-level programming language there is. It's basically the processor's own instructions, written out by hand. Python only handles the window and the buttons. [Point at the four lines at the bottom] Those are the four basic sound shapes our engine can make."

## Slide 2: Pick a preset or move a slider; Assembly builds the sound
Presets
Coin
Laser
Explosion
Jump
Hit
Power-Up
Blip
Randomize
Controls
Waveform: square, sawtooth, triangle, noise
Pitch: start, slide (octaves/s), minimum, vibrato
Envelope: attack, sustain, decay, volume
Noise seed: same seed gives the identical sound
4
waveforms
44.1 kHz
16-bit mono PCM
≤ 5 s
220,500 samples max
Notes: "This is what you see when you use it. There are seven presets, like Coin, Laser and Explosion, plus a Randomize button. Each slider changes one ingredient of the sound: how high or low it is, whether the pitch slides up or down, a little wobble, how long it lasts, and how loud it is. Every time you move something, the sound is rebuilt instantly, the picture of the wave updates, and you can play it or save it as a normal audio file. A bit of background on how digital sound works: a sound is just a long list of numbers. Each number says how far the speaker should push out at that moment. We make 44,100 of those numbers for every second of sound, which is CD quality."

## Slide 3: Three layers, and only the bottom one makes sound
GUI
Python + Tkinter
Sliders, presets, waveform view, Play, Save WAV
Binding
Python ctypes
Fills the 44-byte struct, allocates buffers, turns 0 into an error
Engine sfx.dll
NASM x86-64 Assembly
Computes every sample and builds the WAV bytes
One regeneration, step by step
1
sfx_sample_count
2
allocate buffer
3
sfx_generate
4
sfx_write_wav
5
draw · play · save
Also built: ref/sfx_ref.c, the same algorithm in C. The app never uses it; it is the answer key for tests and the speed baseline.
Notes: "This is the most important slide, so I'll go slowly. Think of a restaurant. [Point left] The Python window is the waiter. It takes your order from the sliders. [Point middle] This middle piece is the order slip. It writes your choices down in a fixed format the kitchen understands. [Point right] And the Assembly engine is the kitchen. It actually cooks the sound. [Point at the five steps] Every click goes through the same five steps: ask the engine how long the sound will be, set aside space for it, fill that space with the sound, wrap it up as an audio file, then show it and play it. We also wrote the exact same recipe a second time in C, which is a more everyday programming language. The app never uses that copy. It's our answer key. We use it to check that the Assembly gets every single number right, and to compare speed."

## Slide 4: A 44-byte struct is the contract between Python and Assembly
+0
waveform
0–3
+4
base_freq
20–4000 Hz
+8
slide
±4 oct/s
+12
min_freq
20–1000 Hz
+16
vib_depth
0–0.5
+20
vib_rate
0–30 Hz
+24
attack
0–2 s
+28
sustain
0–2 s
+32
decay
0–3 s
+36
volume
0–1
+40
seed
≠ 0
uint32 float32 Each box = 4 bytes. 11 × 4 = 44 bytes.
Written three times, must match byte for byte
NASM
struc SfxParams
engine/sfx.asm
C
typedef struct SfxParams
ref/sfx.h
Python
class SfxParams(ctypes.Structure)
gui/sfx_binding.py
Notes: "Python and Assembly don't speak the same language, so they need a shared form to fill in. [Point at the row of boxes] This is that form. It has eleven boxes in a fixed order: things like which wave shape, the starting pitch, how long the fade-out is, and the volume. Every box is exactly the same size, so the whole form is 44 bytes. A byte is just the basic unit of computer memory. The Assembly side doesn't know any of the names. It only knows positions. It's like saying 'look at the seventh box' instead of 'look at the fade-in time'. That's why we wrote this layout three times, once per language, and they have to match perfectly. And if anything on the form is out of range or doesn't make sense, the engine refuses to make the sound and just reports an error. It never crashes."

## Slide 5: Three exported functions follow the Windows x64 calling rules
sfx_sample_count
Validate every field, compute length
In: RCX = params
Out: EAX = planned samples
sfx_generate
The synthesizer loop
In: RCX = params
RDX = out
R8D = capacity
Out: EAX = samples written
sfx_write_wav
44-byte header + copy samples
In: RCX = samples
EDX = count
R8 = out
R9D = capacity
Out: EAX = bytes written
Returns 0 on any error: NULL pointer, invalid parameter, buffer too small
Used by the engine (volatile)
Free to overwrite; the caller expects them to change
RAX RCX RDX R8–R11 XMM0–XMM5
Never touched (non-volatile)
RBX RBP RSI RDI R12–R15 XMM6–XMM15
Nothing to save or restore; verified by tests/abi_probe.asm
Notes: "Our engine does exactly three jobs. [Point at each box in turn] One: tell me how long this sound will be. Two: actually make the sound. Three: turn it into a proper audio file. Windows has strict rules about how programs pass information to each other: where each piece of information goes, and where the answer comes back. We follow those rules exactly, and that's what the small print on these boxes shows. [Point at the bottom] The bottom part is about good manners. The processor has a small number of super-fast storage slots. Windows says some of them are yours to scribble on, and some you have to hand back exactly as you found them. Our engine only ever uses the ones it's allowed to scribble on, so it never has to back anything up. We also wrote a separate test that checks we really do leave the others untouched."

## Slide 6: Every sample passes through 7 steps, 44,100 times per second
1
Slide pitch
freq ×= MULT
cap at 20 kHz
end if below min_freq
2
Vibrato
256-entry sine table
vib = 1 + depth × sine
3
Advance phase
phase += freq × vib / 44100
wrap at 1.0
4
Shape
square, sawtooth,
triangle or noise
5
Envelope
attack 0 → 1
sustain 1
decay 1 → 0
6
Quantize
× gain × volume × 32767
round: cvtss2si
clamp: packssdw
7
Store
out[n] = sample
n++ and loop
Registers that live across the whole loop
R8D
n, sample index
XMM3
phase 0–1
XMM4
frequency (Hz)
XMM5
vibrato phase
R9D
noise state
Notes: "This is the heart of the program. The engine runs one loop, and every lap of the loop produces one of those numbers we talked about. So it runs 44,100 times for every second of sound. [Run your hand along the seven steps] On each lap it does seven small jobs. One: nudge the pitch up or down a tiny bit if the sound is meant to slide. If it slides too low, the sound just ends early. Two: add a small wobble to the pitch, called vibrato. Three: move forward through the wave. Four: work out the shape: square, sawtooth, triangle or noise. Five: apply the volume fade, meaning fade in, hold, fade out. Six: convert it into the number format audio files use. Seven: save it and go round again. The important values stay inside the processor the whole time instead of going back and forth to memory, and that's why it's fast."

## Slide 7: Four waveforms come from one phase value between 0 and 1
Square
phase < 0.5 ? +1 : −1
comiss + jb
Sawtooth
2 × phase − 1
mulss, subss
Triangle
1 − 4 × |phase − 0.5|
andps clears the sign bit = abs()
Noise
new random value each cycle
xorshift32 × 2⁻³¹
phase = how far through one cycle (0 to 1). Frequency only changes how fast phase moves, so slides and vibrato stay smooth.
Notes: "So how do we get four different shapes? We keep track of one number called the phase. The easiest way to picture it is a clock hand. It starts at the top, goes round, and after one full lap it's back at the start. Every wave shape is just a simple rule for turning the clock position into a height. [Point at each drawing] Square: high for the first half of the lap, low for the second half. Sawtooth: a steady ramp up, then a drop. Triangle: up, then back down. Noise: a random height that changes once every lap. The nice thing is that changing the pitch only changes how fast the clock hand moves, so pitch slides and wobbles stay smooth."

## Slide 8: Six Assembly techniques that C would have hidden from us
1
NaN-proof validation
comiss xmm0,[low]
jp .bad
NaN sets the parity flag; 9 fields checked by one table-driven loop
2
Pitch slide without pow()
2^x ≈ 1 + y + y²/2
SSE has no exponent instruction; error ≈ 10⁻¹⁴, below float precision
3
Phase accumulator
minss xmm4,[maxfreq]
20 kHz cap keeps the step < 1, so one subtraction always wraps
4
abs() with a bit mask
andps xmm2,[absmask]
0x7FFFFFFF clears the float sign bit for the triangle wave
5
Clipping for free
packssdw xmm0,xmm0
Saturates to −32768..32767: loud samples clip, never wrap
6
Repeatable noise
x^=x<<13; x^=x>>17; x^=x<<5
Xorshift32: same seed, same sound; seed 0 rejected
Notes: "These are six problems that a normal programming language solves for you behind the scenes. In Assembly, we had to solve them ourselves. [Point at each box as you go] One, bad input. If someone sends a value that isn't even a real number, comparisons behave strangely, so we added an extra check that catches it. Two, no power button. The processor has no built-in way to do 'two to the power of something', which pitch slides need, so we used a short maths shortcut. It's accurate because each step is tiny. Three, the clock hand. We cap the pitch at 20,000 vibrations a second, so the hand can never skip more than one lap at a time. Four, making numbers positive. There's no built-in way to do that for decimals, so we use a trick that switches off the minus sign directly. Five, too loud. If a value goes over the maximum, we clip it at the maximum instead of letting it wrap round to a big negative number, which would make a nasty click. Six, random but repeatable. Our noise uses a tiny random-number recipe, so the same starting number always gives exactly the same sound. That's what lets us test it."

## Slide 9: All state lives in registers and one 152-byte stack frame
sfx_generate stack frame (sub rsp,152)
+152
return address
+80–151
spare
+76
NOISE
+72
MULT (slide)
+68
STEP (vibrato)
+64
D (decay)
+60
AS (attack+sustain)
+56
A (attack)
+52
TOTAL
+48
CAP
+40
OUT pointer
+32
P params pointer
+0–31
shadow space
RSP →
152-byte frame
152 = 9×16 + 8 restores 16-byte alignment after the return address; well under the 256-byte budget
Reentrant and thread-safe
No writable globals; 100 concurrent calls from Python all correct
Self-contained DLL
5,632 bytes, 0 imported DLLs, every section read-only
Windows unwind info
.pdata/.xdata describe the frame so Windows can walk the stack through sfx_generate
Notes: "Where does the engine keep its working data while it runs? Only two places. One is the processor's own storage slots. The other is one small scratch area, 152 bytes, that it borrows while it works and gives back when it's done. Think of a sticky note you throw away afterwards. [Point at the diagram] Windows is fussy about the size and position of that scratch area, and 152 is the number that fits its rules. Because the engine doesn't keep anything permanently, lots of parts of a program can use it at the same time without getting in each other's way. We tested a hundred at once. The whole engine file is tiny, about 5.6 kilobytes, and it doesn't depend on anything else."

## Slide 10: sfx_write_wav wraps the samples in a 44-byte WAV header
0
RIFF
4
36+size
8
WAVE
12
fmt
16
16
20
PCM, mono
24
44100 Hz
28
88200 B/s
32
2 B, 16 bit
36
data
40
size = 2n
44+
samples…
Byte offset shown on top. Amber fields are patched per sound; the rest is a constant template in .rdata.
1
Check
both pointers, 1 ≤ n ≤ 220,500, capacity ≥ 44 + 2n
2
Copy header
44 bytes from the template
3
Patch sizes
byte 40 = 2n; byte 4 = 2n + 36
4
Copy samples
2n bytes after the header; return 44 + 2n
lea r10d,[rdx*2+44] computes the file size 44 + 2n in one instruction
Notes: "The last job is turning all those numbers into a real audio file, a WAV file, the kind any media player can open. A WAV file starts with a short label that tells the player things like 'this is CD quality, one channel'. [Point at the strip] That label is the same every time except for two numbers, highlighted here, which say how big the file is. So the engine copies a ready-made label, fills in those two numbers, puts the sound right after it, and that's a finished file. Python then plays it or saves it."

## Slide 11: Assembly matches the C reference bit for bit on 10,000 sounds
1,279,144
native checks passed
0
max sample difference vs C
10,000
random parameter sets
1,000
repeat runs, byte-identical
Engine tests (C harness)
Invalid input: out of range, NaN, ±infinity, seed 0, NULL
Guard bytes: nothing written past the buffer
441 Hz tone has 440–441 cycles; slide timing ±1%
WAV header byte-for-byte at 1, 44,100, 220,500 samples
abi_probe.asm: non-volatile registers untouched
Python and GUI tests
1,000 Randomize presses, 0 engine errors
100 concurrent engine calls
Off-screen GUI: slider to redrawn waveform, median 80.8 ms (target 100 ms)
Every preset generates and saves a valid WAV
Notes: "So how do we know it actually works? Remember the answer-key copy written in C. We made 10,000 random sounds plus 20 hand-picked ones, including every preset, and compared every single number from our Assembly with the answer key. That's about 1.28 million checks. Our requirement allowed a tiny difference of one; we got zero differences. We also tried to break it. We fed it bad values, checked it never writes outside the space it was given, checked the audio file label one byte at a time, and checked that a tone meant to be 441 vibrations a second really is."

## Slide 12: Under 5 ms everywhere; a tested one-line fix nears C -O2
Chart: Median time to generate 1 s of sound (ms)
| Square | Sawtooth | Triangle | Noise
Assembly (first build) | 0.35 | 1.58 | 1.68 | 0.33
Assembly + movaps fix | 0.26 | 0.35 | 0.4 | 0.24
C -O2 | 0.31 | 0.32 | 0.4 | 0.26
C -O0 | 0.94 | 1.71 | 2.05 | 0.96
4.5×
faster sawtooth from one changed instruction
Cause: movss on line 161 made each sample wait for the last one
Fix: movaps copies the whole register, so the wait disappears
Tested: all 1,279,144 checks pass, max difference still 0
Median of 1,000 runs after 100 warm-ups; 44,100 samples, slide + vibrato on; one Ryzen 9 8940HX laptop
Notes: "Now speed. We timed how long it takes to make one second of sound, did that a thousand times, and took the middle result. [Point at the chart] Our goal was under 5 milliseconds, which is five thousandths of a second. Every shape beats that easily. Here's the interesting part. [Point at the red bars] Our first version was noticeably slower than the C version on two of the shapes, sawtooth and triangle. We dug into why, and it came down to one single line of code. That line copied a number in a way that made the processor wait for the previous sample to completely finish before it could start the next one. It's like a queue where nobody can move until the person in front is done. We swapped that line for a different copying instruction that doesn't cause the wait. [Point at the green bars] Those two shapes got about four and a half times faster, roughly the same speed as C, and all 1.28 million correctness checks still passed."

## Slide 13: What we have not proven yet, and what comes next
Known limits
Benchmarks from one laptop; background apps and power not controlled
No group listening test yet: presets not claimed recognisable
Noise changes once per cycle, so it sounds slightly muffled
movaps speed-up measured in one session; matching C -O2 not yet shown on other CPUs
Playback in real players (Audacity, Media Player) still to confirm
Next steps
1
Benchmark on a second laptop on AC power
2
Group listening test and 10-minute soak test
3
Rerun the C comparison on another CPU
4
Visible-window GUI review by another member
Notes: "We also want to be upfront about what we haven't proven yet. All our timings come from one laptop. We haven't done a proper listening test with other people, so we're not claiming the presets sound perfect to everyone. The noise sound is a little muffled, which was a trade-off we chose to keep things simple. And the speed-up from that one-line change was measured in one session, so we'd want to repeat it on another computer. [Point right] These are our next steps."

## Slide 14: Live demo, then questions
Coin → Laser → Explosion → Randomize → Save WAV
Run: launch.bat · Rebuild: build.bat · Tests: python tools/run_checks.py
Notes: "Let me show you it working." [Click Coin] "That's a short beep that slides up in pitch, like picking up a coin." [Click Laser] "This one slides down fast, which gives you the laser sound." [Click Explosion] "This is noise that drops in pitch with a long fade-out." [Press Randomize twice] "Randomize sets every slider to something random, and the sound is rebuilt instantly." [Click Save WAV] "And this saves it as a normal audio file. [Point at the bar at the bottom] Down here it shows how long the sound is and how many milliseconds our engine took to make it. Thank you. We're happy to take questions."